Microscope information sheet (updated on 10 Aug 2022)

System name: DeltaVision Elite Microscope

(Installed 27 June 2009. SN cn62532-original, WMI asset # A002159)

Location: Microscopy Lab 3 (J2.12A) WIMR building

Microscope: Inverted Olympus IX-71 (microscope base replaced 14 July 2009)

Illumination: Insight SSI (ultra fast solid state illumination). LED transmitted light module for DIC.

Camera: CoolsSnapHQ2 (Roper Scientific) and EMCCD (model c11-1024-M-LVDS-16-AC)

Computer: OEM (Operating: CentOS 7). Replaced 10 Mar 2020.

Software: Resolve3D and Softworx 6.5.2 acquisition and integrated deconvolution software (on Linux CentOS 7 platform)

Objectives:

- Olympus 10X: UPLSAPO 10x NA 0.4 WD 3.1mm (Recycled from FV 1000 confocal) (ID: 14)

- Olympus 20X: UPLSAPO 20x NA 0.75 WD 0.6mm (Ordered 20Dec2016) (ID: 10211, pn=1-U2B825, api#34-018019-121)

- Olympus 40X: UPlanFLN 40x Oil NA 1.30 WD 0.2mm (originally ordered 20Dec2016 but damaged product so refund by GE Health Oct 2018) (ID: 10416, pn=1-U2B530, api#53-850009-122)

- Olympus 60X: PlanApo 60x Oil NA 1.42, WD 0.15mm (replaced in Oct 2018) (ID: 10612, pn=1-U2B933, api#34-018019-110)

- Olympus 100X: U-PLAN-Apo 100x Oil NA 1.4, WD 0.12mm (ID: 10007, pn=1-U2B836, api#53-850009-110)

|  | Objective | Type | Numerical Aperture | Pixel Size (um/pixel) | Working Distance (mm) | Lens ID | Position in Turret | Color Coding | Rubber Band Color | Condensor Position | Colar Correction |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 10x | Olympus UPLSAPO | Dry | 0.4 | 0.6626 | 0.31 | 14 | 1 | Yellow | None | 3 | NA |
| 20x | Olympus UPLSAPO | Dry | 0.75 | 0.3219 | 0.6 | 10211 | 2 | Green | None | 3 | NA |
| 40x | Olympus UPlanFLN | Oil | 1.3 | 0.1601 | 0.2 | 10416 | 3 | Light Blue | Blue | 3 | NA |
| 60x | Olympus Plan Apo | Oil | 1.42 | 0.1069 | 0.15 | 10612 | 4 | Dark Blue | Green | 4 | NA |
| 100x | Olympus U-Plan Apo | Oil | 1.4 | 0.0644 | 0.12 | 10007 | 5 | White | Purple | 5 | NA |

Fluorescent filters:

| Standard Filter | Excitation (nm) | Emission (nm) | Polychroic filter position |
| --- | --- | --- | --- |
| 1: DAPI | 390/18 | 435/48 | DAPI/FITC/TRITC/Cy5: 1 (SemRock: 52-852111-000) |
| 2: FITC | 475/28 | 523/36 |  |
| 3: TRITC/Alexa594 | 543/27 (575/25) | 594/45 (632/60) | DAPI/FITC/Alex594/Cy5: 2 (SemRock: 52-852112-000) |
| 4: Cy5 | 632/22 | 676/34 |  |
| Live Cell Filter | Excitation (nm) | Emission (nm) |  |
| 1: CFP | 438/24 | 470/24 | CFP/YFP: 5 (SemRock: 52-852109-000) |
| 2: YFP | 475/28 | 559/38 |  |
| 3: GFP | 515/10 | 525/50 | GFP/mCherry: 4 (SemRock: 52-8513444-000, Rev B, C136902) |
| 4: mCherry | 575/25 | 632/60 | GFP/mCherry: 6 (SemRock: 52-861344-000, Rev B, C137306) |

Data storage: see the policy print located next to the phoneset in the lab.

Other computer software

Internet connection: yes

Contact:        Dr. Hui Zhang

Email: hui.zhang@wimr.org.au

Phone: 8627 3212

Example description of microscope application and data processing:

For image acquisition z–stacks of 0.2 μm increments were collected using a UPLSAPO 100× oil (1.40NA) objective on a Deltavision Elite Microscope (Image Solutions – Applied Precision, GE Health) attached to a CoolSNAP HQ2 CCD camera. Deconvolution and other image processing were performed using SoftWoRx Suite 2.0 (Applied Precision, GE) and Illustrator (Adobe Systems Inc., USA).